## Slide 1: Chemical waste disposal: protect the environment and save money!
Phillip Crisp and Eva Crisp

## Slide 2: Chemical Disposal
The quantity of chemical wastes generated in a school is insignificant
(compared with agriculture, mining and industry)
HOWEVER
Wastes can pose hazards, if stored poorly
A school is an educational institution
• Attitudes adopted during youth continue into adulthood
• Proper training should be given to those who will later be decision makers

## Slide 3: The improvement process
eliminate unwanted chemicals
redesign procedures to minimize waste production, e.g. spot reactions, recycling, destruction, less toxic chemicals
dispose of wastes LEGALLY SAFELY by - sewer - garbage - waste collection service

## Slide 4: THE LAW
Follow all
* WA laws
* local government/authority regulations
instead of the advice in RiskAssess
whenever there is conflict between the two

## Slide 5: Water Corporation
Laboratory chemical waste
https://www.watercorporation.com.au/Help-and-advice/Trade-waste/Trade-waste-in-your-business/Other-industries/Laboratory-chemical-waste
• chemicals of major concern
• waste avoidance and minimisation
• best management practices & specific requirements
Laboratory waste from schools
http://www.labnetwest.asn.au/wp-content/uploads/2020/06/Laboratory-waste-from-schools.pdf
Acceptance criteria for trade waste
https://www.watercorporation.com.au/Help-and-advice/Trade-waste/Permits/Trade-waste-permits/Acceptance-criteria-for-trade-waste
• substances subject to acceptance criteria
acceptance criteria for common waste components
acceptance criteria for heavy metals (metropolitan)

## Slide 6: Waste Authority
• WasteSorted Schools program
https://www.wasteauthority.wa.gov.au/wss/
programs, resources, grants, accredited schools
Household Hazardous Waste free dropoff
https://www.wasteauthority.wa.gov.au/programs/view/household-hazardous-waste
items that can and can’t be dropped off
school laboratory garbage?

## Slide 7: Chemical wastes in schools
Aqueous liquid wastes
• dissolved salts
• acidic or basic
• suspended particles
Water-miscible organic wastes
alcohols, e.g. methylated spirits
ketones, e.g. acetone
Water-immiscible organic wastes
• hydrocarbons, e.g. hexane, kerosene
• special chemicals, mostly for organic chemistry
Solid wastes
• precipitates, e.g. BaSO4, Fe oxides
*

## Slide 8
Problems in the sewer!
• toxic metals
e.g. Hg, Cd, Pb, As, . . . VERY BAD Cu, Ni, Co, . . . BAD since contaminate sludge $$$
• toxic persistent organic chemicals
e.g. pesticides since contaminate sludge $$$
• highly acidic/alkaline liquids since may damage pipes
• flammable liquids (water-immiscible) since may cause an explosion!

## Slide 9
Aqueous liquid wastes
Pour down the sewer ONLY if the ‘acceptance criteria’ of the Water Corporation are met (known for metropolitan schools).
Otherwise, an environmentally responsible approach:
• neutralize to ~pH 6.5-8.5 (natural waters)
• only “safe” amount of each chemical down the drain
in order to minimise environmental harm from treated sewage when it is released into river or ocean.
All wastes exceeding a “safe” amount of a chemical should be retained for a waste collection service.
WHAT IS SAFE?

## Slide 10: Estimation of “safe” quantities*
Consider the cation and anion in a salt separately.
Toxicity of a salt is dominated by the most toxic ion:
e.g. lead chloride, potassium dichromate
Some ions should not go down the drain at all
e.g. Hg2+, Pb2+, Cd2+, . . .
while others are ok almost without (school) limit
e.g. Na+, Ca2+, Cl-, SO42-, . . .
and other ions in between
* RiskAssess “Disposal of chemical wastes”, in Learning Resources

## Slide 11: Tabulation and calculation
“Safe” disposal quantity for an ion for a class:
0 – 1000 g/day
Copper sulfate
copper: 1 g/day [Very toxic to aquatic life
with long lasting effects]
sulfate: 1000 g/day. [In solid laundry detergent]
Therefore, copper sulfate: 1 g/day (as solid or solution)
Enough for some spot tests down the drain.
Beyond that, wastes need to be collected!

## Slide 12: Comparison (g/day) to sewer
Element Water Corporation* RiskAssess
Arsenic 1 0
Cadmium 1 0
Chromium 30 (10)** 10
Copper 30 (10)** 1
Lead 30 (10)** 0
Mercury 0.1 (1)** 0
Molybdenum 1 1
Nickel 6 (10)** 1
Selenium 1 1
Silver 2 1
Zinc 50 (10)** 10
* Acceptance criteria for large metropolitan WWTPs only (Beenyup, Subiaco and Woodman Point); otherwise, case by case
** Water Corporation “Laboratory chemical waste”, criteria for treatment before discharge

## Slide 13: Organic liquid wastes
Water-miscible
e.g. methylated spirits, acetone
Dilute 1 part to 20 parts water, then down the drain.
Prevents explosive air/vapour mixture.
Microorganisms in sewer will consume the chemicals.
Water-immiscible
e.g. hexane, kerosene
Retain for collection by waste service.
Separate hydrocarbon waste from halogenated waste.

## Slide 14: Waste processing
Collection
Large bottles (e.g. 2.5 L ‘Winchesters’) correctly labelled, funnel at top (fume cupboard)
Treatment
Only if time, equipment and skilled people available
Disposal
To maximum recommended daily quantity:
• down the drain or into garbage
Otherwise, retain for waste collection
SEPARATE CONTAINER FOR EACH WASTE!

## Slide 15: Solid wastes
Only material of a domestic nature
is allowed to be disposed of in the garbage
Consider
transport of garbage
leaching from landfill
Geologically-stable minerals
(precipitated during reactions)
e.g. barium sulfate (baryte)
No leaching of toxic chemicals in a domestic landfill.

## Slide 16: Purpose of disposal advice
• improves understanding of harmful properties
• focuses on avoiding serious environmental harm
• reduces the cost of waste collection service
• provides a learning tool for staff and students
• promotes care for the environment

## Slide 17: RiskAssess Advice
Individual chemical advice in ‘Disposal’ SUBSCRIBER for each of >3000 chemicals and solutions
‘Disposal of chemical wastes’ FREE https://www.riskassess.com.au/docs/DisposalOfChemicalWastes.pdf
‘Chemical waste containers’ FREE https://www.riskassess.com.au/info/waste_containers
‘Labels for chemical waste containers’ FREE https://www.riskassess.com.au/info/waste_container_labels
‘How to dispose of chemical wastes ’ SUBSCRIBER In: ‘Safety in Schools’ book, chapter C7

## Slide 19: Labelling and storage of wastes
All wastes must be
• labelled according to GHS, and
• stored according to Dangerous Goods Class.
Flammable wastes in a flammable liquids cabinet!
Place each toxic waste in a SEPARATE container!
Recommend both:
large RA label with GHS information
large blank label for hand-writing the quantity and identity of each waste added to the container

## Slide 20: RiskAssess pre-prepared waste labels
Labels for 25 common wastes ready to print
Based on the likely compositions and likely maximum concentrations
Otherwise, use Custom Labels,
especially if wastes are less hazardous

## Slide 21: DEMONSTRATION
• Learning resources
• Examples
• Waste treatment and recycling
• Labels
QUESTIONS
team@riskassess.com.au