## Slide 1: Chemical Waste Disposal
Phillip Crisp and James Crisp

## Slide 2: Chemical Disposal
The quantity of chemical wastes generated in a school is insignificant.
HOWEVER
• A school is an educational institution
• Attitudes adopted during youth continue into adulthood
• Proper training should be given to those who will later be decision makers

## Slide 3: The improvement process
eliminate unwanted chemicals
redesign procedures to minimize waste production, e.g. spot reactions, recycling, destruction, less toxic chemicals
dispose of wastes LEGALLY SAFELY by - sewer - garbage - waste collection service

## Slide 4: THE LAW
Follow all
* WA laws
* local government/authority regulations
instead of the advice in RiskAssess
whenever there is conflict between the two

## Slide 5: Water Corporation
Laboratory chemical waste
https://www.watercorporation.com.au/Help-and-advice/Trade-waste/Trade-waste-in-your-business/Other-industries/Laboratory-chemical-waste
• chemicals of major concern
• waste avoidance and minimisation
• best management practices & specific requirements
Laboratory waste from schools
http://www.labnetwest.asn.au/wp-content/uploads/2020/06/Laboratory-waste-from-schools.pdf
Acceptance criteria for trade waste
https://www.watercorporation.com.au/Help-and-advice/Trade-waste/Permits-and-charges/Trade-waste-permits/Acceptance-criteria-for-trade-waste
• substances subject to acceptance criteria
acceptance criteria for common waste components
acceptance criteria for large metropolitan WWTPs

## Slide 6: Waste Authority
• Waste Wise Schools program
https://www.wasteauthority.wa.gov.au/wws
Household Hazardous Waste free dropoff
https://www.wasteauthority.wa.gov.au/programs/view/household-hazardous-waste
school laboratory garbage?

## Slide 7: Chemical wastes in schools
Aqueous liquid wastes
• dissolved salts
• acidic or basic
• suspended particles
Water-miscible organic wastes
alcohols, e.g. methylated spirits
ketones, e.g. acetone
Water-immiscible organic wastes
• hydrocarbons, e.g. hexane, kerosene
• special chemicals, mostly for organic chemistry
Solid wastes
• precipitates, e.g. BaSO4, Fe oxides
*

## Slide 8
Problems in the sewer!
• toxic metals
e.g. Hg, Cd, Pb, As, . . . VERY BAD Cu, Ni, Co, . . . BAD since contaminate sludge $$$
• toxic persistent organic chemicals
e.g. pesticides since contaminate sludge $$$
• highly acidic/alkaline liquids since may damage pipes
• flammable liquids (water-immiscible) since may cause an explosion!

## Slide 9
Aqueous liquid wastes
Pour down the sewer ONLY if the criteria of the water authority are met.
Otherwise, an environmentally responsible approach:
• neutralize to ~pH 6.5-8.5 (natural waters)
• only “safe” amount of each chemical down the drain
in order to minimise environmental harm from treated sewage when it is released into river or ocean.
All wastes exceeding a “safe” amount of a chemical should be retained for a waste collection service.
WHAT IS SAFE?

## Slide 10: Estimation of “safe” quantities*
Consider the cation and anion in a salt separately.
Toxicity of a salt is dominated by the most toxic ion:
e.g. lead chloride, potassium dichromate
Some ions should not go down the drain at all
e.g. Hg2+, Pb2+, Cd2+, . . .
while others are ok almost without (school) limit
e.g. Na+, Ca2+, Cl-, SO42-, . . .
and other ions in between
* RiskAssess “Disposal of chemical wastes”, in Learning Resources

## Slide 11: Tabulation and calculation
“Safe” disposal quantity for an ion for a class:
0 – 1000 g/day
Copper sulfate
copper: 1 g/day [Very toxic to aquatic life
with long lasting effects]
sulfate: 1000 g/day. [In solid laundry detergent]
Therefore, copper sulfate: 1 g/day (as solid or solution)
Enough for some spot tests down the drain.
Beyond that, wastes need to be collected!

## Slide 12: Comparison (g/day) to sewer
Element Water Corporation* RiskAssess
Arsenic 1 0
Cadmium 1 0
Chromium 30 10
Copper 30 1
Lead 30 0
Mercury 0.1 0
Molybdenum 1 1
Nickel 6 1
Selenium 1 1
Silver 2 1
Zinc 50 10
* Acceptance criteria for large metropolitan WWTPs

## Slide 13: Organic liquid wastes
Water-miscible
e.g. methylated spirits, acetone
Dilute 1 part to 20 parts water, then down the drain.
Prevents explosive air/vapour mixture.
Microorganisms in sewer will consume the chemicals.
Water-immiscible
e.g. hexane, kerosene
Retain for collection by waste service.
Separate hydrocarbon waste from halogenated waste.

## Slide 14: Aqueous waste containers
Cations
Large bottles half-filled with 110 g/L Na2CO3
e.g. Cd, Co, Cu, Pb, Hg, Ni, Zn ions
Large bottle half-filled with 180 g/L NaCl
e.g. silver ions
Anions
Large bottle half-filled with 150 g/L FeSO4
e.g. chromate ions
Large bottle half-filled with 350 g/L CaCl2
e.g. fluoride ions
SEPARATE CONTAINER FOR EACH ION !

## Slide 15: Solid wastes
Only “material of a domestic nature”
is allowed to be disposed of in the garbage
Consider
transport of garbage
leaching from landfill
Geologically-stable minerals
(precipitated during reactions)
e.g. barium sulfate (baryte)
No leaching of toxic chemicals in a domestic landfill.

## Slide 16: Labelling and storage of wastes
All wastes must be
• labelled according to GHS, and
• stored according to Dangerous Goods Class.
Especially:
Flammable wastes in a flammable liquids cabinet!
Place each toxic waste in a SEPARATE container!
Most easily, use RiskAssess labels:
standard labels for single-component wastes
custom labels for multicomponent wastes

## Slide 18: Purpose of disposal advice
• focuses on avoiding serious environmental harm
• reduces the cost of waste collection service
• decreases emphasis on less harmful substances
• provides a learning tool for staff and students
• promotes care for the environment

## Slide 19: Current disposal advice
Free Learning resources:
• ‘Disposal of Chemical Wastes’ document
• this presentation (for teaching others)
Within RiskAssess:
• ‘Safety in Schools’ book, chapter C7:
‘How to dispose of chemical wastes’

## Slide 20: Future disposal advice: advice for each individual chemical
• advice for each of the 3000 chemicals/solutions
• following logic of ‘Disposal of Chemical Wastes’
• under ‘Standard handling procedures’
• no need to calculate for each chemical/solution
• dedicated waste container information
• simplify disposal and save money
• completion early 2021 (Big job!)

## Slide 21
CHEMICAL SPILLS
Deal with injured persons
Prevent further injuries
Seek assistance e.g. Emergency 000
. . . . . . . . . . . . . . . . . . . . . . . . . . . .
• Contain the spill
• Clean up the spill
• Render spilled material harmless

## Slide 22
Procedures for chemical spills
• Acids
• Alkalis
• Organic solvents
• Mercury
• Solids

## Slide 23
Spills kit
Rubber gloves
Safety goggles
Mop and bucket
Dust pan and brush
Four 5 L plastic buckets
Plastic shovel
10 kg kitty litter (dried bentonite clay NOT paper)
2 kg sodium bicarbonate
2 kg calcium hydroxide
(10 kg dry sand)
(2 kg sulfur for mercury decontamination)
Paper towels
NOTE:
Keep in front of chemical store!

## Slide 25: What is RiskAssess?
• web-based risk assessment tool
• customised to the school situation
• provides - electronic templates (AU/ISO) - database information on risks (chemical, equipment, biological) - equipment ordering/lab scheduling - labelling (GHS)
- learning resources
• easy sharing of experiment templates for customisation

## Slide 27: Logic
• separate sections for teacher and laboratory technician
• initial assessment of inherent risk - if low, go to end - if medium or more, record control measures - if high or extreme, third reviewer required
• cross-checking by teacher/labtech/reviewer
• scheduling, ordering, labelling to save time
• inexpensive ($250+GST per campus per year)

## Slide 28: Electronic system
• relatively rapid
• prompts sensitive to context
• reduces paper consumption
• easy to review and update
• easy monitoring and statistics
• easy storage
• demonstrated to work in schools
RiskAssess: 2250 schools AU+NZ+CA
WA: 45 (13%)
3,700,000 risk assessments

## Slide 29: Details
• access from school/home
• nothing to install on computer, tablet or phone (instant update)
• unlimited number of simultaneous users and risk assessments
• minimal data entry See brochure!
• complements SDSs
• continuing input from science staff
• multiple backups of data & backup server
• support and advice

## Slide 30: Advantages of RiskAssess
• proper consideration of risks and control measures
• standardisation
• storage of records for legal purposes
• communication between teachers and laboratory technicians
• discourages spur-of-the-moment experiments
• useful for new/inexperienced staff

## Slide 31: Even more!
• scheduling system
• prac ordering
• GHS labelling - standard - customised
And an exciting new video . . .
“Getting Started with RiskAssess”
starring Phillip and Eva!